Finite Element Modelling of Gyroid-based Honeycomb

---
Aims and Objectives
- Complete Finite Element analysis of proposed gyroid geometry will be performed.
- Open-source tools are exploited.
- Finite Element framework is established for analysing
  displacement and stress fields.
- Open-source frameworks are indispensable tools to handle state of the art geometries for FE modelling.
- This statement wanted to be proven in this study.

---
Flowchart
Geometry Generation
Mesh Generation
Definition of Boundary Conditions
Finite Element Analysis
Visualization

---
Flowchart - Tools
Geometry Generation
Python & FreeCAD
Mesh Generation
GMSH
Definition of Boundary Conditions
DOLFINX
Finite Element Analysis
DOLFINX
Visualization
Paraview

---
Geometry Generation
Here are the steps;
- Python script generates points.
- Reading these points from txt file and import them into FreeCAD.
- Manipulate geometry to get Gyroid-based honeycomb.
  The process is fully automated.

---
Geometry Generation
50mm
50mm

---
Mesh Generation
Around ~667k cells

---
Definition of Boundary Conditions
Displacement
boundary condition
Rest of the boundaries;
Traction-Free
Fixed Boundary

---
Finite Element Analysis
- Dolfinx Framework has been used.
  https://github.com/FEniCS/dolfinx
- Linear Elasticity equations are solved.
- Python interface has been utilized.

---
Material Properties

---
Visualization – Displacement Field
We are imposing y=-0.01m displacement from top boundary
(Compression Test)

---
Visualization – Von Mises Stresses

---
Issue - Overlapping
When displacement of the top boundary exceeds y = -0.02m, the mesh overlaps.
Contacts between internal boundaries should be defined to avoid overlapping.
Possible solutions;
1) This problem can be treated as postprocessing problem.
As we now the displacements of the each node in the mesh, we can	manipulate the coordinates accordingly.
At the moment, this is not implemented in Dolfinx,
But we can implement -> it will take some time for sure (it is already ongoing PostDoc project of friend of mine).

---
Conclusion
- Framework of Finite Element Analysis for Gyroid-based honeycomb geometry is established.
- Material parameters are not well-defined yet, but easily doable.
- More complex structures (graded, periodic) can be implemented using Python scripts.